# Introduction

This book is a manual of PX-35 equipped with the Bluetooth communication application program.Please refer to "2.Bluetooth test Application manual" when you want to confirm the operation of the Bluetooth communication.Please refer to "3. the scanner test" when you want to confirm the reading speed of the scanner.The function of the system menu has been described in "4.System menu manual".

# Bluetooth test Application manual

2-1 Start Application

At power supply OFF: When some keys are pushed, the application is started.

System menu is started: When “Restart” is selected, the application is started.

2-2 Connection method

1.The communication setting is set pressing [1][2][3]KEY.

2.When [4]KEY is pressed, Bluetooth is connected.

Master: A peripheral Bluetooth equipment is retrieved, and the list display is done. It connects it with the selected address.

Slave:  It shifts to connected waiting state.

Please connect it from the Bluetooth equipment.

3. When the bar code is read while communicating Bluetooth, the reading data is transmitted.

※Reading slows to the extent that it communicates, and use the following scanner test mode at systemmenu, please when you want to confirm the response.

2-3 End Application

Please start up the system menu, and select Power Off.

# Scanner Test

3-1 Start Scanner Test

Push [UP],[DOWN],[TRG] KEY and start System menu.

Push [UP] [DOWN] KEY, and selects “Diagnostics->Scanner” with [Trigger] or [ENT] KEY.

3-2 Scanner Test function

The read data is displayed on the screen.

Two kinds of modes change if UP is pressed while the scanner test is starting.

The single reading mode : When the trigger is pressed, the bar code is read. (about one second)

The continuous reading mode :  It keeps reading the bar code.

3-3 End Scanner Test

It ends by the Down button pressing.

# System menu manual

4-1 Start system menu

Power supply OFF　　　　　:  Press [UP] [DOWN] [Trigger] KEY at the same time.

The application is operating　:  Keep Presssing [UP] [DOWN] [Trigger] KEY for one second.

It is started from the head of the system menu (main menu).

## 4-2 End system menu

If you select "Cancell", "Restart" or "Power off" from the main menu,system menu is ended.

When "Cancell" is selected ,it returns to the state immediately before entering the system menu .

When "Reactivation" is selected, The application is started.

It cannot be selected "Cancell" ,if you enter "Terminal test" menu once.

## 4-3 System menu function list

The selection item is changed with [UP] [DOWN] KEY, and it selects it with [Trigger] or [ENT] KEY.

It returns to the previous screen by one when the [CLEAR] KEY is pushed.

Table 1　System menu function list

| Main menu | Sub menu | Content |
| --- | --- | --- |
| Cancel |  | The system menu is ended, and the application does the resume. |
| Restart |  | The system menu is ended. |
| Power Off |  | The system menu is ended, and the power supply is turned off. |
| Download appl. |  | The application is downloaded by using the application loading utility of PC. The application starts when normally ending. It returns to the main menu when terminating abnormally. |
| Copy appl. | Download appl. | The application is downloaded from other equipment. The application starts when normally ending. |
|  | Upload appl. | The application is up-loaded to other equipment. It returns to the copy menu regardless of normal termination/abnormal termination. |
| PC Remote |  | It enters a remote state of PC, and the response from the host side is waited for. |
| Settings | Contrast | The contrast of LCD is adjusted. |
|  | Time & Date | The system date is set. |
|  | Key click | The key click sound is set. |
|  | Terminal id | Terminal ID is set and it confirms it. |
|  | Resume Mode | A setting of the resume effective/invalid is done. |
|  | Auto power | It sets it in the auto power downtime. |
|  | Auto Backlight | The backlight lighting and turning off the display are set. |
|  | Display Battery | The display setting in the state of the battery is done. |
|  | Bluetooth | Bluetooth is set. (Table2) |
|  | Set Default | All of each setting are returned to the state of the factory shipment. |
| Diagnostics | Display | The test of the display is executed. |
|  | Key | The test of the keyboard is executed. |
|  | Memory | The memory is checked. |
|  | Buzzer | The test of the buzzer sound is executed. |
|  | ＬＥＤ | The test of LED is executed. |
|  | Backlight | The backlight is checked. |
|  | Clock | The test at the system date is executed. |
|  | Battery | The main sub-battery voltage is checked. |
|  | Scanner | The test of the scanner is executed. |
|  | Infrared Com. | The sending and receiving test of IrDA is executed. |
|  | Bluetooth | Various tests of Bluetooth. The confirmation is executed. (Table 3) |
| List files | Disk A: | The file list of the random access memory disk is displayed. |
| Show version |  | OS and version information such as BOOT are displayed. |

Table 2　Bluetooth setting menu function list

| Main menu | Sub menu | Content |
| --- | --- | --- |
| Device Select | Manual | The connection destination address is input with the key, and set. |
|  | Discovery | The nearby Bluetooth device is retrieved, it selects from the list, and the connection destination address is set. |
| Input PINcode |  | The PIN code is set. |
| Local name |  | A local name is set. |

Table 3　Bluetooth test menu function list

| Main menu | Sub menu | Content |
| --- | --- | --- |
| Bluetooth SPP | Barcode | The sending and receiving test is executed reading the bar code of the connection destination address. |
|  | Discovery | The nearby Bluetooth device is retrieved, it selects from the list, and the sending and receiving test is executed. |
| RF Power |  | The test of the electric wave transmission is executed. |
| Show version |  | The version and address information on Bluetooth are displayed. |